### What warnings and/or protective measures must be taken when using this equipment?

### SAFE WORK PROCEDURE ………                                                             ………….… ………………   ………… …………..

List actions to be taken and order.

| 1 | Make sure all required PPE is used prior to beginning the task. |
| --- | --- |
| 2 | Pick up your allocated respirator and place it on your head. |
| 3 | Plug the respirator airline into the inlet, located on the top of the air supply filter mounted by the gun cleaning unit. |
| 4 | Lower the shield on the air fed respirator to cover your face. |
| 5 | Remove the spray gun from the wall bracket and then plug it into the airline hanging beneath the air supply filter. |

CLEANING SPRAY GUNS THAT HAVE USED SOLVENT PRODUCTS

| 1 | Turn the gun cleaning unit on and place spray gun inside. |
| --- | --- |
| 2 | Pick up the brush located inside the basin in one hand, and have the spray gun in the other. |
| 3 | Place your foot on the pedal that has a brush icon shown above it, and start cleaning the spray gun with the brush in your hand. |
| 4 | Once the gun has been cleaned with the brush, then pick up the other trigger. |
| 5 | Take your foot from the foot pedal with the brush icon and move it to the one to the right (this will bring clean solvent to the top). |
| 6 | When the gun has been cleaned, it needs to be dried. Use the air blower to dry the gun. To use the automatic cleaner, lift up the rear door and place the spray gun in the desired area and press the automatic pedal. |
| 7 | When completed, unplug the spray gun from the airline. |
| 8 | Unplug the air fed respirator and remove from your head. |

CLEANING SPRAY GUNS THAT HAVE USED WATERBORNE PRODUCTS

| 1 | Place the spray gun in the basin, pull the trigger on the water spray. To rinse the gun press floor pedal to trigger to access water for the brush. |
| --- | --- |
| 2 | When the spray gun has been cleaned, use the air blower to dry the gun. |
| 3 | When completed, unplug the spray gun from the airline. |
| 4 | Unplug the air fed respirator and remove from your head. |

This Standard Operating Procedure does not necessarily cover all possible hazards associated with the equipment. It should be used in conjunction with other references. It is designed as an adjunct to training and to act as a reminder to trained, competent operators.

| ASSESSMENT DATE: / / IF USED AS RECORD OF COMPENTENCY | Verified by Supervisor: |  | (name & signature) |
| --- | --- | --- | --- |
|  | Competent operator: |  | (name & signature) |

Version 1

# Text boxes

### DO NOT USE UNLESS YOU ARE TRAINED, COMPETENT & HAVE PERMISSION

### STANDARD OPERATING PROCEDURE

### Cleaning of Spray Gun