### What warnings and/or protective measures must be taken when using this equipment?

### EQUIPMENT REQUIRED FOR THIS TASK…                                                                                         ….    .…

Fire proof cabinet for storage of paint waste

### SAFE WORK PROCEDURE ………                                                             ………….… ………………   ………… …………..

List actions to be taken and order.

| 1 | Open the doors of the fire proof cabinet and tip all non-catalyst (unable to cure by crosslinking) paint products into designated (solvent / water) waste disposal containers / drums which are located in the fire proof cabinet. The waste disposal drums are clearly identified by labels either waste water or waste solvent. |
| --- | --- |
| 2 | For catalysed (will cross link) products leave on bench and allow to go hard. Once these products are in their cured state, remove products and dispose of in allocated waste disposal drums located in designated area. |
| 3 | When waste water / solvent drums are full they must be sealed and labelled for removal by a registered waste disposal company. |
| 4 | These must be stored in the allocated space. |

This Standard Operating Procedure does not necessarily cover all possible hazards associated with the equipment. It should be used in conjunction with other references. It is designed as an adjunct to training and to act as a reminder to trained, competent operators.

| ASSESSMENT DATE: / / IF USED AS RECORD OF COMPENTENCY | Verified by Supervisor: |  | (name & signature) |
| --- | --- | --- | --- |
|  | Competent operator: |  | (name & signature) |

Version 1

# Text boxes

### DO NOT USE UNLESS YOU ARE TRAINED, COMPETENT & HAVE PERMISSION

### STANDARD OPERATING PROCEDURE

### Disposal of Paint Waste