### What warnings and/or protective measures must be taken when using this equipment?

### POTENTIAL HAZARDS…………                                                                         …………………    ………   … ……….    .…

### What are the potential hazards?   What can go wrong?  Are there known ways in which the equipment could fail generating a hazard?  Are there any by-products from use (i.e. eye hazards, breathing hazards)?

| Falling objects | Entanglement hazards |
| --- | --- |
| Trapping hazards | Crushing hazards |
| Dust and debris in eyes |  |

### PRE-OPERATIONAL SAFETY CHECKS                          do not use defective or faulty equipment                                                                            Equipment is sometimes not used for long periods.  What must be done to ensure that it is always as safe as possible to use?

| 1 | A vehicle hoist must not be operated unless it has a current certificate of inspection. |
| --- | --- |
| 2 | Ensure that vehicle hoist has operating and maintenance instructions permanently located and clearly visible. |
| 3 | Check the capacity of the hoist compared to the weight of the vehicle. If vehicle is too heavy, do not proceed. |
| 4 | Ensure support arms are capable of being locked in position |
| 5 | Ensure rubber pads are in good condition on all load points. |
| 6 | Ensure the area is clean and clear of grease, oil, and objects that may be a slip/trip hazard |

### OPERATIONAL SAFETY…………                                                                   ………….… ………………   ………… …………..

Note things that you must check whilst using the equipment.  Must you be aware of gauges providing important operational information?  How must you respond to certain things if they occur?

| 1 | Centre vehicle on hoist, ensuring that the weight is evenly distributed to the front and rear |
| --- | --- |
| 2 | Identify the correct jacking points and place the lifting pads under the vehicle at the front & rear on the jacking points, ensuring contact |
| 3 | Only one person shall operate the hoist at a time |
| 4 | Ensure hoist area is clear of people and equipment before operating |
| 5 | Never leave the hoist running unattended |
| 6 | Engage manual lock. |
| 7 | At the completion of work lower the vehicle hoist and ensure all equipment is left safe. |

### POST-OPERATIONAL…   ………………………………… …                                                                 ……………… …………

### What must be done to ensure that the equipment will be ready for safe use next time it is required?  Is there routine maintenance to do after use?  What tidying up is required when you have finished using it?

| 1 | Switch off equipment |
| --- | --- |
| 2 | Leave the equipment in a clean and tidy state. |

### FORBIDDEN                                     this equipment must only be used for the purpose for which it is intended

### Are there examples of known prohibited uses?  Could there be temptation to use the equipment for jobs it is unsuitable for.

| 1 | Never leave a vehicle unattended while in operation (raising or lowering). |
| --- | --- |
| 2 |  |

This Standard Operating Procedure does not necessarily cover all possible hazards associated with the equipment. It should be used in conjunction with other references. It is designed as an adjunct to training and to act as a reminder to trained, competent operators.

| ASSESSMENT DATE: / / IF USED AS RECORD OF COMPENTENCY | Verified by Supervisor: |  | (name & signature) |
| --- | --- | --- | --- |
|  | Competent operator: |  | (name & signature) |

# Text boxes

### STANDARD OPERATING PROCEDURE

### Vehicle Hoist Operation - General

### DO NOT USE UNLESS YOU ARE TRAINED, COMPETENT & HAVE PERMISSION